## Slide 1: Robotics architecture

## Slide 2: Architectures
The architecture of a robot defines how the job of generating actions from percepts is organized.
We will largely be concerned with autonomous mobile robots in dynamic environments, for which the need for a sophisticated control architecture is clear.
The design of robot architectures is essentially the same agent design problem.
There is no accepted theory of architecture design that can be used to prove that one design is better than another.

## Slide 3
Classical architecture
By the late 1960s, primitive but serviceable tools for intelligent robots were available.
These included vision systems that could locate simple polyhedral objects; two-dimensional pathplanning algorithms; and resolution theorem provers that could construct simple, symbolic plans using situation calculus.
From these tools, together with a collection of wheels, motors and sensors, emerged Shakey, the forerunner of many intelligent robot projects.
The first version of Shakey, appearing in 1969, demonstrated the importance of experimental research in bringing to light unsuspected difficulties.
https://en.wikipedia.org/wiki/Shakey_the_robot

## Slide 4
The researchers found that general purpose resolution theorem-provers were too inefficient to find nontrivial plans, that integrating geometric and symbolic representations of the world was extremely difficult, and that plans don‘t work.
This last discovery came about because Shakey was designed to execute plans without monitoring their success or failure.
Because of wheel slippage, measurement errors and so on, almost all plans of any length failed at some point during execution.
The second version of Shakey incorporated several improvements.

## Slide 5
First, most of the detailed work of finding paths and moving objects was moved from the general problem-solving level down into special-purpose programs called intermediate-level actions (ILAs).
These actions in fact consisted of complex routines of low-level actions (LLAs) for controlling the physical robot, and included some error detection and recovery capabilities.
For example, one ILA called NAvTo could move the robot from one place to another within a room by calling the A* algorithm to plan a path and then calling LLAs to execute the path, doing some path corrections along the way.
The LLAs were also responsible for updating the internal model of the world state, which was stored in first-order logic.

## Slide 6
Motion errors were explicitly modelled, so that as the robot moved, its uncertainty about its location increased.
Once the uncertainty exceeded a threshold for safe navigation, the LLA would call on the vision subsystem to provide a new position fix.
The key contribution of the ILA/LLA system, then, was to provide a relatively clean and reliable set of actions for the planning system.
The planning system used the STRIPS algorithm, essentially a theorem-prover specially designed for efficient generation of action sequences.
STRIPS also introduced the idea of compiling MACRO-OPERATORS the results of planning into generalized macro-operators,

## Slide 7
The entire system was controlled by PLANEX, which accepted goals from the user, called STRIPS to generate plans, then executed them by calling the specified ILAs.
PLANEX kept track of the current world state, comparing it to the preconditions of each subsequence in the original plan.
After each action completed, PLANEX would execute the shortest plan subsequence that led to a goal and whose preconditions were satisfied.
In this way, actions that failed would be retried, and fortunate accidents would lead to reduced effort.
If no subsequence was applicable, PLANEX could call STRIPS to make a new plan.

## Slide 8
The basic elements of Shakey's design—specialized components for low-level control and geometric reasoning, a centralized world model for planning, compilation to increase speed, and execution monitoring to handle unexpected problems—are repeated in many modern systems.
Compilation, or explanation-based learning, has been used extensively in two robot architectures: Robo-SOAR (Laird et al., 1991) and THEO (Mitchell, 1990).
https://en.wikipedia.org/wiki/Soar_(cognitive_architecture)
https://www.cs.cmu.edu/~tom/pubs/theo_framework_1989.pdf
Computation times for simple tasks can be reduced from several minutes to less than a second in some cases.
In both of these architectures, compilation is invoked whenever a problem is solved for which no ready-made solution was available.

## Slide 9
In this way, the robot gradually becomes competent and efficient in routine tasks, while still being able to fall back on general-purpose reasoning when faced with unexpected circumstances.
Much of the research in robotics since Shakey was switched off has been at the level of ILAs and LLAs.
Shakey was able to move on a flat floor, and could push large objects around with difficulty.
Modern robots can twirl pencils in their fingers, screw in screws and perform high-precision surgery with greater accuracy than human experts.

## Slide 10
Soar is a cognitive architecture, originally created by John Laird, Allen Newell, and Paul Rosenbloom at Carnegie Mellon University.
It is now maintained and developed by John Laird's research group at the University of Michigan.
The goal of the Soar project is to develop the fixed computational building blocks necessary for general intelligent agents – agents that can perform a wide range of tasks and encode, use, and learn all types of knowledge to realize the full range of cognitive capabilities found in humans, such as decision making, problem solving, planning, and natural-language understanding.